## Slide 1
HH
SORYBOARD
Last revision: 02. June. 2020

## Slide 2
Select an asset:
- ASSET 01
- ASSET 02
- ASSET 03
- ASSET 04
- …
SCREEN_01
SCREEN_02
Long-press the power button on your HH device to turn it on.
GREEN LED lights indicate that the HH device is ON.
Press the “CONFIRM” button to confirm that your HH device is on.
Select your HH device:
- HH DEVICE 01
- HH DEVICE 02
- HH DEVICE 03
- HH DEVICE 04
- …
SCREEN_03
Confirm

## Slide 3
Selected Asset:
SAMPLE ASSET
Selected HH Device:
SAMPLE HH DEVICE
Press the button on your device HH to start the process.
In the first step you will place the NDE sensor on the motor.
SCREEN_04
SCREEN_05
BLUE LED light indicates the first part that needs to be detached.
Release the small clamp and unscrew the sensor. Red underside = NDE
Place the sensor on the motor’s NDE.
Press the button on your HH device to continue process.
In the next step you will place the DE sensor on the motor.

## Slide 4
SCREEN_06
BLUE LED light indicates the first part that needs to be detached.
Release the small clamp and unscrew the sensor. Blue underside = DE
Place the sensor on the motor’s DE.
Press the button on your HH device to to continue process.
In the next step the sensors will start collecting data and you will take temperature measurements.

## Slide 5
SCREEN_07
Blinking GREEN LED lights indicate that the sensors are taking vibration measurements.
Point the laser at the motor and press the button on the HH device to take temperature measurements.
Press the “NEXT” button to continue process.
In the next step you will reassemble your HH device.
Next

## Slide 6
SCREEN_08
Blinking GREEN LED lights indicate that the sensors are taking vibration measurements.
Point the laser at the motor and press the button on the HH device to take temperature measurements.
Press the “NEXT” button to continue process.
In the next step you will reassemble your HH device.
Next

## Slide 7
SCREEN_09
Reassemble your HH device. Red to red, blue to blue.
Press the button on your HH device to to continue process.
In the next step your HH device will send the measurements to the smart sensor app.
DATA TRANSFER IN PROGRESS
Please do not turn off your HH device.
SCREEN_10
50 %
App navigates to operational parameters card of the asset.

## Slide 8
ERROR_SCREEN_R
ERROR_SCREEN_NR
We encountered an error. This is indicated by the RED LED lights.
Follow these steps to resolve this error:
- STEP 01
- STEP 02
- STEP 03
- STEP 04
- …
RESOLVABLE ERROR
NON-RESOLVABLE ERROR
We encountered an error. This is indicated by the RED LED lights.
Long-press the power button on your HH device to turn it off and
press the “RESTART PROCESS” button.
!
X
Restart Process